## Slide 1
TA: Eunjin Lee
Email: eunjin_lee@korea.ac.kr
Single-Cycle ARM Processor Design 2nd Term Project
Single-cycle Processor

## Slide 2: Overview
Instruction Analysis
Control Signal Analysis
Module Implementation
1st Term Project
2nd Term Project

## Slide 3: Overview
ARMProcessor.v
ControlUnit.v
RegisterFile.v
Extend.v
ALU.v

## Slide 4: Overview

## Slide 5: Overview
Given processor can run following instructions
  Branch : B, BL
  Arithmetic : ADD, SUB, CMP, MOV
  Load/Store : LDR, STR
Given processor can run following suffixes
  Logical : EQ, NE (‘Z’ in ‘NZCV’)
Addressing Modes
  Addressing Mode 1 : 1 (immediate), 2 (register)
  Addressing Mode 2 : 1 (immediate offset), 2 (register offset)

## Slide 6: Overview
1) Instruction fetch (Clock 0’s posedge)
2) Check condition code & Initialize control signal
3) Register read (Clock 90’s posedge)
4) ALU
After ALU operation: Update NZCV
5) Memory read / write (Clock 0’s negedge)
6) Register write (Clock 90’s negedge)
1)
Clock 0: blue, Clock 90: red
2)
3)
4)
5)
6)
(Clock 0 is memory-related, Clock 90 is register file-related)
1 Clock Cycle
Clock

## Slide 7: Module
ARMProcessor module
  Input
    clk : Clock 90
    reset : 1 if press “KEY0” button
    inst[31:0] : current instruction
    readdata : data from memory
  Output
    pc : instruction address (starting at 0)
    be[3:0] : 1111(2) (default) – don’t change!
    memaddr[31:0] : data address
    memread : 1(2) (default) – don’t change!
    memwrite : specify whether memory is to be written
    writedata[31:0] : write data to memory

## Slide 8: Module
RegisterFile Module
  Register 14 ($14) – Link Register (LR)
    This register holds the address of the next instruction after a Branch and Link instruction
    $14 = PC + 4
  Register 15 ($15)
    It can be used in most instructions as a pointer to the instruction which is two instructions after the instruction being executed
    $15 = PC + 8
PC (It is different with Register 15($15))
  PC (next instruction) = PC (current instruction) + 4

## Slide 9: Module
Extend Module
  Data Processing Type: zero extended-imm8
    0000/1010(2) -> 0000/0000/0000/0000/0000/0000/0000/1010(2)
  Load/Store Type: zero extended-imm12
    0000/1010/0000(2) -> 0000/0000/0000/0000/0000/0000/1010/0000(2)
  Branch Type: sign-extended-imm24, shifting left two bits
    1000/0000/0000/0000/1010/0000(2) -> 1111/1110/0000/0000/0000/0010/1000/0000(2)
    0000/0000/0000/0000/1010/0000(2) -> 0000/0000/0000/0000/0000/0010/1000/0000(2)

## Slide 10: Control signal
RegSrc
  RegSrc[0] = “0” : ADD, SUB, CMP, MOV, LDR, STR
    Using Register[inst(19:16)]
  RegSrc[0] = “1” : B, BL
    Using Register[15] for calculating branch target address

## Slide 11: Reference
Single-cycle processor in ARM
  https://cs631.cs.usfca.edu/guides/single-cycle-processor
  https://pages.hmc.edu/harris/class/e85/old/fall19/lect19.pdf
  https://redirect.cs.umbc.edu/~jtang/archives/cs411.f21/lectures/L12SingleCycleControl.pdf
Verilog https://www.chipverify.com/verilog/verilog-tutorial