## Slide 1
Computer Architecture
Assignment #1: ARM Instruction Analysis
Eun Jin Lee (eunjin_lee@korea.ac.kr)
Intelligent Computer Architecture & Systems Lab.

## Slide 2
To understand hardware instructions and assembly language
To understand ARM instructions through the ARM reference manual
To understand how instructions are executed at the system and hardware level
Purpose of Assignment #1

## Slide 3: About report
ARM instruction analysis report
  Analyze instruction of address 000~024 in instruction file(inst_data.mif)
    Change hex instructions to binary format and translate the binary instructions to assembly codes by referring to the ARM reference manual
    Explain the meaning of each instruction
    Explain the actual execution flow of the instructions
    Explain where the execution ends (if it doesn’t end, explain the range of repetition in detail)
Instruction of addr. 000
Binary format result
Which instruction it is
Meaning
Instruction of addr. 024
Binary format result
Which instruction it is
Meaning
. . .
Actual Execution Sequence
Where the execution ends
(Or repetition range)
For the whole execution
For each instruction

## Slide 4: inst_data.mif
address
(HEX)
instruction
(HEX)
EA000006

## Slide 5: arm_architecture_reference_manual.pdf

## Slide 6: Example
EA000006
  Change instructions to binary format
    1110 1010 0000 0000 0000 0000 0000 0110 (2)
  Translate the binary instructions to assembly codes by referring to the reference file
    B #8;
  Describe what instruction means
    Move to the address PC*4+8+6x4 (In the case of RISC-V, add 4 to PC)
      PC means the address of instruction currently being executed
      Because the address unit is 4 Byte (= 1 Word)
    Therefore, move to the address (0 + 8 + 24) / 4 = 008
      Next instruction will be E59F2EC8 at the address 008

## Slide 7: Example
EAFFFFFE
  Change instructions to binary format
    1110 1010 1111 1111 1111 1111 1111 1110 (2)
  Translate the binary instructions to assembly codes by referring to the reference file
    B #1;
  Describe what instruction means
    Sign-extending the 24-bit signed(two’s complement) immediate to 30 bits
      1111 1111 1111 1111 1111 1110 —> 11 1111 1111 1111 1111 1111 1111 1110
    Shifting the result left two bits to form a 32-bit value
      1111 1111 1111 1111 1111 1111 1111 1000 = -210 * 4 = -810
    Adding this to the contents of the PC, which contains the address of the branch instruction plus 8 bytes
      Make ‘4’ by adding the current instruction address ‘(1*4)+8’ and ‘-8’
      Divide 4 into 4 so that it branches at first among the word-unit instructions
      (= Because it branches to the same instruction, the same instruction repeats indefinitely)
Step 1: Switching 0 to 1, 1 to 0
0000 0000 0000 0000 0000 0010
1111 1111 1111 1111 1111 1101
Step 2: Add 1 to the result of 1st Step
1111 1111 1111 1111 1111 1101
1
1111 1111 1111 1111 1111 1110
cf. -2 = 1111 1111 1111 1111 1111 1110
= 2’s complement of 0000 0000 0000 0000 0000 0010

## Slide 8: Example
E59FDE78
  Change instruction to binary format
    1110 0101 1001 1111 1101 1110 0111 1000 (2)
  Translate the binary instructions to assembly codes by referring to the reference file
    LDR $13, [$15, #0xE78];
    Mark it as # because I bit, the 25th bit, is 0
  Describe what instruction means
    Calculate the address of memory by adding the value stored in the 15th register with #0xE78
    Access to the calculated memory address and load the data into the 13th register
    Read the value saved in address [$15 + #0xE78] of memory and store it $13

## Slide 9: Example
E1A0F00E
  Change instruction to binary format
    1110 0001 1010 0000 1111 0000 0000 1110 (2)
  Translate the binary instructions to assembly codes by referring to the reference file
    MOV $15, $14;
  Describe what instruction means
    Store the value of the 14th register at the 15th register

## Slide 10
Hint
Condition Code (e.g., 0(0000) = Equal, E(1110) = Always)
  Refer to ARM Reference Manual p.112
Data Processing Instructions (e.g., MOV, CMP)
  Opcode: Refer to Manual p.115
  Instruction Encoding: Refer to Manual p.116
Load and Store Instructions (e.g., LDR, STR)
  Address Mode: Refer to Manual p.129
  Instruction Encoding: Refer to Manual p.130
  Examples: Refer to Manual p.131
Branch Instructions (e.g., B, BL)
  Instruction Encoding: Refer to Manual p.160
  Examples: Refer to Manual p.114

## Slide 11: Differences in the ARM and RISC-V instructions

## Slide 12: Differences Between ARM and RISC-V
Different instruction field format is used
  RISC-V (R-type)
  ARM
What is “cond” field?
31
25
24
20
19
15
12
11
0
7
6
14
func7
rs2
rs1
func3
opcode
rd
7 bits
5 bits
5 bits
3 bits
5 bits
7 bits
31
28
27
26
25
24
21
20
19
16
15
12
11
0
0 0
I
opcode
S
Rn
Rd
operand
4 bits
2 bits
4 bits
4 bits
4 bits
12 bits
1
bit
1
bit
cond

## Slide 13: Differences Between ARM and RISC-V
Condition Field
Refer to ‘arm_architecture_reference_manual.pdf’ A3.2.1

## Slide 14: Differences Between ARM and RISC-V
Condition Code Flag
  Program Status Registers
    SPSR(Saved Progam Status Register), CPSR(Current Program Status Register)*
  N - set if the result is negative
  Z - set if the result is zero
  C - set if carry exists in the results of addition, subtraction, shift (unsigned operation)
  V - set if the result overflows from addition or subtraction (signed operation)
  Operation with “S” suffix
    ADDS, SUBS (ADD, SUB doesn’t update flags)**
The 1st value == The 2nd value
The 1st value - The 2nd value = 0
==> Z is set.
*Refer to A2.5 in manual
Format
Condition Code Flags
**Refer to A4.1.3 in manual

## Slide 15: Execution Flow
Example
  Consider following ARM assembly
MOV
>> R0 is 2
CMP
>> ‘N’ is set after this instruction because ‘r0 - 3 < 0’ is true.
ADDLT
>> This line is executed because ‘cond’ field is met; r0 is now 3.
CMP
>> ‘Z’ is set because ‘r0 == 3’ is true
ADDLT
>> This line is not executed because the ‘cond’ field is not met.
BEQ
>> This line is executed because ‘Z’ is met.
Syntex
N | Z | C | V
r0

## Slide 16: Differences Between ARM and RISC-V
Branch instruction
  RISC-V
    Branching condition is tested and executed in one instruction
  ARM
    Branching condition is embedded in condition(cond) field
    Branch is executed only if “cond” condition is met

## Slide 17: Instruction Set Manual of ARM and RISC-V
ARM
  https://iitd-plos.github.io/col718/ref/arm-instructionset.pdf
RISC-V
  https://riscv.org/wp-content/uploads/2019/06/riscv-spec.pdf

## Slide 18: Announcement

## Slide 19: About Assignment #1
Report: 5 points
  Analyzing instruction at 000~024 address in the instruction file (inst_data.mif)
Report should include the following
  Student number and name
  For each instruction,
    Change the instruction from HEX to Binary (Score: 1)
    Translate the binary instructions to assembly codes by referring to the ARM reference manual and explain the meaning of each instruction (Score: 2)
  Explain the actual execution flow of the instructions (Score: 1)
  Specify where the execution ends (if not, specify the range repeated in detail) (Score: 1)

## Slide 20: About Assignment #1
Write your answers by editing blue colored part.

## Slide 21: Submission
Due date
  October 28 (Fri) 11:59 P.M.
How to submit
  Through KULMS
  Report
  Submission format
    Compress the file as ‘CA1_STUDENTNUMBER_NAME.pdf’
    (Export to PDF file from .docx)

## Slide 22: Q&A
If you have any questions about Assignment #1, feel free to email TA (eunjin_lee@korea.ac.kr)